## Slide 1
Adapter For Expression Pedals
Amon Benson | Sensor and Actuator Systems | Milestone Meeting 1 | 28. September 2026
https://media.sweetwater.com/m/insync/2018/08/keyboardexpression.jpg

## Slide 2
Motivation
https://media.sweetwater.com/m/insync/2018/08/keyboardexpression.jpg
https://thumbs.static-thomann.de/thumb/padthumb600x600/pics/bdb/_19/195660/7223134_800.jpg
Notes: Expression (sometime Volume) Pedals are used during live performances to alter the sound of an audio signal
Example image: guitarist, can apply audio filter/modify frequence with both hands free
Compared to a switch pedal: Set a specific position and drive continuous values
Goal of this project: Create a hardware adapter to connect these pedals to a PC

## Slide 3
Motivation
https://thumbs.static-thomann.de/thumb/padthumb600x600/pics/bdb/_19/195660/7223134_800.jpg
Notes: Simple passive device consisting of a single potentiometer
Complexity comes from the fact that no standard pinout exists
Nearly all pedals use a 6.35 mm TRS jack, two common pinouts
Some only use Tip-Ring plug
Sometimes pedals themselves have a switch to toggle between two common configuration
 Build a device that can:
  detect the specific configuration of an attached pedal
  continously read its position and send that to the host PC via the MIDI-USB protocol

## Slide 4
Detection Process
Notes: Model: Two resistors A and B
If we apply our positive and negative supply, we can read the voltage in the middle
 Detect the resistor ratio and therefore the pedal position
Order of taps unknown: Test all possible permutations  Solve for the exact resistor values
To do this electrically

## Slide 5
Detection Process
+3.3V
GND
Tap 1
Tap 2
Tap 3
Notes: Each Tap can be pulled High, Low, or left floating
Each Tap is connected to a separate ADC channel

## Slide 6
Circuit Design – Analog Frontend
Tap 1
Tap 2
Tap 3
(unused)
Notes: Simple passive Anti-Aliasing-Filter: ~1.6 kHz
Pullup/down: Tristate Buffer IC (SN74)
  Two control signals per output  74HC shift register (Microcontroller GPIO expansion)

## Slide 7
Circuit Design – ADC
ADC 1.1 ADC 1.2 ADC 1.3
ADC 1.4
ADC 2.1
ADC 2.2
…
Notes: ADC: AD7124
Low speed (< 1kHz)  Sigma Delta
Works with 3.3V supply (Microcontroller logic level)
Interface via SPI
Minimal external circuitry required

## Slide 8
Circuit Design – Microcontroller
Notes: uC: Raspberry Pi Pico 2 Module
Bare RP2040 chip  USB, crystal, flash, etc. would all need to be added manually. Pico 2 Module is the official (well tested hardware)
STM32 (F4/G4/L4)  Faster CPU, but more external hardware required + proprietary USB stack

## Slide 9
Circuit Design – Power Supply
Digital Supply (3.3V)
Digital Supply (5V)
Analog Supply (3.3V)
Notes: Digital supplies (5V and 3.3V)
  3.3V can be toggled between this LDO and the Pico Module’s onboard voltage regulator
Analog supply
  GND connected via single star point

## Slide 10
Circuit Design – DC Input Protection
Notes: Reverse polarity protection circuit via an ideal diode
TVS protection diode for voltage spikes

## Slide 11
Hardware
  circuit design
  PCB layout and routing
  manufacturing
Firmware
  planning of the detection algorithm
  implementation using the microcontroller toolchain
  simulation of ADC measurements for offline (functional) testing
Outlook
Notes: Hardware
  Finish during the next week
  Pick exact parts
  Decoupling of the ADC
  Hardware buttons and LEDs for indication purposes
  Routing
Firmware
  Start software implementation simultaneously next week
  Offline simulation of the detection algorithm using ideal ADC measurements

## Slide 12
power supply quality
SPI signal quality
functional self-test
  SPI device inquiry (ADC)
  tristate buffer
detection algorithm for known static networks
accuracy and linearity
end-to-end latency
Testing and Evaluation Plan
Notes: Measure voltage and SNR on the supply rails
Measure signal integrity of the SPI bus
Self-tests: SPI device id inquiry, tristate buffer pullup/pulldown using ADC
Detection algorithm for known networks
  Apply a resistor configuration and validate the detected topology
  Also apply edge cases where R=0 Ohm (short or open circuit)
Sweep a precision resistor and compare the measured resistor ratio to the actual one
Measure end-to-end latency from input resistance change to the value arriving at the USB host

## Slide 13
[1] M. Frejek, "AVR-Transistortester," Embedded Projects Journal, no. 11, 2011. Online documentation: K.-H. Kübbeler. [Online]. Available: https://www.mikrocontroller.net/articles/AVR-Transistortester
[2] Mission Engineering, "Understanding expression pedals." [Online]. Available: https://missionengineering.com/understanding-expression-pedals/
[3] Analog Devices, AD7124-8: 8-Channel, Low Noise, Low Power, 24-Bit, Sigma-Delta ADC with PGA and Reference, Data Sheet, Rev. F, 2023. [Online]. Available: https://www.analog.com/media/en/technical-documentation/data-sheets/ad7124-8.pdf
[4] Texas Instruments, ADS8688: 16-Bit, 8-Channel, Integrated Analog Front-End SAR ADC, Data Sheet. [Online]. Available: https://www.ti.com/product/ADS8688
[5] Raspberry Pi Ltd., Raspberry Pi Pico 2 Datasheet (RP2350), 2024. [Online]. Available: https://pip-assets.raspberrypi.com/categories/1005-raspberry-pi-pico-2/documents/RP-008299-DS-2-pico-2-datasheet.pdf
[6] Texas Instruments, SN74LVC126A: Quadruple Bus Buffer Gate With 3-State Outputs, Data Sheet. [Online]. Available: https://www.ti.com/lit/ds/symlink/sn74lvc126a.pdf
[7] Analog Devices, ADP7142: 40 V, 200 mA, Low Noise, CMOS LDO Linear Regulator, Data Sheet, Rev. K. [Online]. Available: https://www.analog.com/media/en/technical-documentation/data-sheets/adp7142.pdf
[8] P. Horowitz and W. Hill, The Art of Electronics, 3rd ed. Cambridge, U.K.: Cambridge University Press, 2015.
[9] W. Kester, J. Bryant, and M. Byrne, "MT-031 Tutorial: Grounding Data Converters and Solving the Mystery of 'AGND' and 'DGND'," Analog Devices, Rev. A, 2008.
Sources

## Slide 14
“AVR-Transistortester”
https://content.instructables.com/F4V/9O1Y/IFCDEPNY/F4V9O1YIFCDEPNY.jpg
Notes: Similar principle: “Transistor tester”