## Slide 1
Adapter For Expression Pedals
Amon Benson | Sensor and Actuator Systems | Milestone Meeting 2 | 8. Juli 2026
https://media.sweetwater.com/m/insync/2018/08/keyboardexpression.jpg

## Slide 2
Recap
https://thumbs.static-thomann.de/thumb/padthumb600x600/pics/bdb/_19/195660/7223134_800.jpg
Notes: Expression Pedal = Potentiometer that can be controlled by a footpedal
Used mainly in live audio
Complexity comes from the fact that no standard pinout exists
Device to detect and support all possible pinouts and resistance values
 The device needs to
  detect the specific configuration of an attached pedal
  continously read its position and send that to the host PC via the MIDI-USB protocol

## Slide 3
Detection Process
Notes: Model: Two resistors A and B
How do we detect which tap is connected to which part of this network?
More general form: three-terminal resistive network
 Introduction of a third resistor

## Slide 4
Detection Process
Notes: If this general model of 3 resistors is a potentiometer, one of the resistors must be 0 Ohm, while the others form the voltage divider
By measuring which resistor is 0 Ohm, we know which pin is the wiper

## Slide 5
Detection Process
+3.3V
GND
Tap 1
Tap 2
Tap 3
Live Demo: https://amonbenson.github.io/topology-sim
Notes: Each Tap can be pulled High, Low, or left floating
Each Tap is connected to a separate ADC channel
Live Demo

## Slide 6
Hardware
  schematic design
  build a working prototype (single channel)
  PCB layout and routing
  manufacturing
Firmware
  simulation of ADC measurements for (functional) testing
  implementation and refinement of the detection algorithm
  implementation of the detection algorithm using the microcontroller toolchain
Outlook
Notes: Hardware
  Parts ordered for the prototype
  Started working on it (but not presentable yet)
  Routing
Firmware
  Simulator will not be refined further
  Start implementation on the Raspberry Pi Pico
NEXT PAGE: END!!!

## Slide 7
[1] M. Frejek, "AVR-Transistortester," Embedded Projects Journal, no. 11, 2011. Online documentation: K.-H. Kübbeler. [Online]. Available: https://www.mikrocontroller.net/articles/AVR-Transistortester
[2] Mission Engineering, "Understanding expression pedals." [Online]. Available: https://missionengineering.com/understanding-expression-pedals/
[3] Analog Devices, AD7124-8: 8-Channel, Low Noise, Low Power, 24-Bit, Sigma-Delta ADC with PGA and Reference, Data Sheet, Rev. F, 2023. [Online]. Available: https://www.analog.com/media/en/technical-documentation/data-sheets/ad7124-8.pdf
[4] Texas Instruments, ADS8688: 16-Bit, 8-Channel, Integrated Analog Front-End SAR ADC, Data Sheet. [Online]. Available: https://www.ti.com/product/ADS8688
[5] Raspberry Pi Ltd., Raspberry Pi Pico 2 Datasheet (RP2350), 2024. [Online]. Available: https://pip-assets.raspberrypi.com/categories/1005-raspberry-pi-pico-2/documents/RP-008299-DS-2-pico-2-datasheet.pdf
[6] Texas Instruments, SN74LVC126A: Quadruple Bus Buffer Gate With 3-State Outputs, Data Sheet. [Online]. Available: https://www.ti.com/lit/ds/symlink/sn74lvc126a.pdf
[7] Analog Devices, ADP7142: 40 V, 200 mA, Low Noise, CMOS LDO Linear Regulator, Data Sheet, Rev. K. [Online]. Available: https://www.analog.com/media/en/technical-documentation/data-sheets/adp7142.pdf
[8] P. Horowitz and W. Hill, The Art of Electronics, 3rd ed. Cambridge, U.K.: Cambridge University Press, 2015.
[9] W. Kester, J. Bryant, and M. Byrne, "MT-031 Tutorial: Grounding Data Converters and Solving the Mystery of 'AGND' and 'DGND'," Analog Devices, Rev. A, 2008.
Sources

## Slide 8
power supply quality
SPI signal quality
functional self-test
  SPI device inquiry (ADC)
  tristate buffer
detection algorithm for known static networks
accuracy and linearity
end-to-end latency
Testing and Evaluation Plan
Notes: Measure voltage and SNR on the supply rails
Measure signal integrity of the SPI bus
Self-tests: SPI device id inquiry, tristate buffer pullup/pulldown using ADC
Detection algorithm for known networks
  Apply a resistor configuration and validate the detected topology
  Also apply edge cases where R=0 Ohm (short or open circuit)
Sweep a precision resistor and compare the measured resistor ratio to the actual one
Measure end-to-end latency from input resistance change to the value arriving at the USB host

## Slide 9
“AVR-Transistortester”
https://content.instructables.com/F4V/9O1Y/IFCDEPNY/F4V9O1YIFCDEPNY.jpg
Notes: Similar principle: “Transistor tester”

## Slide 10
Recap
https://media.sweetwater.com/m/insync/2018/08/keyboardexpression.jpg
https://thumbs.static-thomann.de/thumb/padthumb600x600/pics/bdb/_19/195660/7223134_800.jpg
Notes: Expression (sometime Volume) Pedals are used during live performances to alter the sound of an audio signal
Example image: guitarist, can apply audio filter/modify frequence with both hands free
Compared to a switch pedal: Set a specific position and drive continuous values
Goal of this project: Create a hardware adapter to connect these pedals to a PC

## Slide 11
Circuit Design – Analog Frontend
Tap 1
Tap 2
Tap 3
(unused)
Notes: Pullup/down: Tristate Buffer IC (SN74)
  Two control signals per output  74HC shift register (Microcontroller GPIO expansion)

## Slide 12
Circuit Design – ADC
ADC 1.1 ADC 1.2 ADC 1.3
ADC 1.4
ADC 2.1
ADC 2.2
…
Notes: ADC: AD7124
Low speed (< 1kHz)  Sigma Delta
Works with 3.3V supply (Microcontroller logic level)
Interface via SPI
Minimal external circuitry required

## Slide 13
Circuit Design – Microcontroller
Notes: uC: Raspberry Pi Pico 2 Module
Bare RP2040 chip  USB, crystal, flash, etc. would all need to be added manually. Pico 2 Module is the official (well tested hardware)
STM32 (F4/G4/L4)  Faster CPU, but more external hardware required + proprietary USB stack

## Slide 14
Circuit Design – Power Supply
Digital Supply (3.3V)
Digital Supply (5V)
Analog Supply (3.3V)
Notes: Digital supplies (5V and 3.3V)
  3.3V can be toggled between this LDO and the Pico Module’s onboard voltage regulator
Analog supply
  GND connected via single star point

## Slide 15
Circuit Design – DC Input Protection
Notes: Reverse polarity protection circuit via an ideal diode
TVS protection diode for voltage spikes